## Slide 1: I.O.T & A.I. when small things meet big things
Dr.Pasidth Thanachotanankul (DBA,MBA,EE)
PS Evolution Ltd.
4-12-2025

## Slide 2: Table of contents (A.M.)

## Slide 3: Table of contents (P.M.)

## Slide 4
The ESP32 comes in three distinct forms: System on Chip (SoC), Module, and Development Boards (Devkits)

## Slide 6: ESP32 – micro controler

## Slide 12: 🎯 Top 5 สิ่งที่ต้องทำ
ไฟเลี้ยงที่ดี (40% ของความเสถียร) แหล่งจ่าย 5V 2-3A
Capacitor 100µF + 0.1µF ทุกจุด
Ground เดียวกันหมด
2. Watchdog Timer (20%)

## Slide 13
3. Wi-Fi Stability (15%)
4. Error Handling (15%) ตรวจสอบ Free Heap
Handle Exceptions
Auto Recovery
5.หลีกเลี่ยง Strapping Pins (10%) ไม่ใช้ GPIO 0, 2, 12, 15 (ESP32)
ไม่ใช้ GPIO 0, 3, 45, 46 (ESP32-S3)

## Slide 16: Sensors
PZEM ย่อมาจาก "Peacefair Electronic Meter" ซึ่งเป็นชื่อยี่ห้อของเซ็นเซอร์วัดพลังงานไฟฟ้าดิจิทัลสำหรับใช้กับไมโครคอนโทรลเลอร์ เช่น Arduino, NodeMCU อุปกรณ์ PZEM มีหลายรุ่น แต่ละรุ่นจะวัดค่าทางไฟฟ้าที่แตกต่างกัน เช่น แรงดัน (Voltage), กระแส (Current), กำลังไฟฟ้า (Power) และพลังงานไฟฟ้า (Energy) โดยโมดูล PZEM-004T เป็นรุ่นที่นิยมใช้มากที่สุดสำหรับการวัดไฟกระแสสลับ (AC)
คุณสมบัติและลักษณะการทำงาน
วัดค่าทางไฟฟ้า: สามารถวัดค่าต่างๆ ได้ เช่น แรงดันไฟฟ้า (V), กระแสไฟฟ้า (A), กำลังไฟฟ้า (W) และพลังงานไฟฟ้า (Wh)
การวัดกระแสแบบไม่ต้องตัดสาย: ใช้ CT (Current Transformer) แบบหนีบคล้องสายไฟ ทำให้สะดวกและปลอดภัย
ไม่ต้องตัดต่อสายไฟ
การสื่อสาร: สื่อสารกับไมโครคอนโทรลเลอร์ผ่านโปรโตคอล UART (Serial)
การแยกไฟสูง-ต่ำ: มีออปโต้คัปเปลอร์ (Opto-coupler) เพื่อแยกวงจรแรงดันไฟฟ้าสูงออกจากวงจรไมโครคอนโทรลเลอร์ เพิ่มความปลอดภัย

## Slide 17: Switch

## Slide 18: RS485
โมดูล RS485 เป็นส่วนประกอบอิเล็กทรอนิกส์ที่ใช้สำหรับการสื่อสารข้อมูลแบบอนุกรมในระยะไกล (สูงสุด 1,200 เมตร) ในสภาพแวดล้อมทางอุตสาหกรรมที่มีสัญญาณรบกวน
หน้าที่: อำนวยความสะดวกในการสื่อสารข้อมูลที่แข็งแกร่งระหว่างอุปกรณ์หลายตัวบนเครือข่ายบัส
การใช้งานทั่วไป: ระบบอัตโนมัติในโรงงานอุตสาหกรรม, ระบบควบคุมอาคาร และการตรวจสอบระยะไกล

## Slide 19
Multi-purpose IOT Monitoring
(MIM-01)

## Slide 20
Pressure
Stream Flow
Temp & Humi
Water Level
PLC
Vibration Sensor

## Slide 21: Example

## Slide 22
PZEM: Rx => D17
Tx => D16
Relay => D12

## Slide 23: Micro-python

## Slide 28
Workshop #1: wifi_relay.py
https://github.com/drpasidth/esp32_pzem/blob/main/wifi_relay.py
Defines
Functions
Loop
import machine
from machine import Pin
import network
import time
# WiFi credentials
WIFI_SSID = “xxxxxxxxx"
WIFI_PASSWORD = “xxxxxxxx"
# Relay setup
HAS_RELAY = False
relay = None
try:
relay = Pin(12, Pin.OUT)
relay.value(1)
HAS_RELAY = True
except Exception as e:
print("Relay init failed:", e)
HAS_RELAY = False
# Create WLAN object
wlan = network.WLAN(network.STA_IF)
wlan.active(True)

## Slide 29
def connect_wifi():
wlan = network.WLAN(network.STA_IF)
wlan.active(True)
if not wlan.isconnected():
print("Connecting to WiFi...")
wlan.connect(WIFI_SSID, WIFI_PASSWORD)
# Wait up to 10 seconds for connection
for _ in range(10):
if wlan.isconnected():
print("Connected!")
print("IP address:", wlan.ifconfig()[0])
return True
print("Waiting for connection...")
time.sleep(1)
return wlan.isconnected()

## Slide 30
# Main execution
if connect_wifi():
print("WiFi connected successfully")
if HAS_RELAY and relay:
for _ in range(3):
relay.value(1)
time.sleep(1) # Fixed: use time.sleep(), seconds not ms
relay.value(0)
time.sleep(1)
while True:
print("Connected to WiFi")
time.sleep(5)
else:
print("Failed to connect to WiFi")
Infinite loop

## Slide 31: Workshop 2: Esp32-pzem
https://github.com/drpasidth/esp32_pzem/blob/main/esp32-pzem_v2.py

## Slide 32
File esp32-pzem_v2.py
Defines
Functions
Main Loop
Pzem_init()
Pzem_calculate_crc()
Pzem_read_registers()
Pzem_read_all()
Lcd_write()
Lcd_init()
Etc.
Initialization => Reading Loop every 5 seconds.

## Slide 36: Workshop #3 esp32-pzem-webserver.py
https://github.com/drpasidth/esp32_pzem/blob/main/esp32%3Dpzem-webserver.py

## Slide 37
Module Breakdown
1. WiFi Manager (connect_wifi, start_ap_mode, save/load_wifi_config)
  Loads saved credentials from wifi_config.txt, defaults to TP-Link_5B9A
  Tries to connect for 15 seconds
  If fails: Starts Access Point mode (ESP32-PZEM-Setup / 12345678)
  Web setup page at /setup allows entering new credentials → saves & reboots

## Slide 38
Parameter | Register | Conversion
Voltage | 0x0000 | ÷10 (V)
Current | 0x0001-0x0002 | ÷1000 (A)
Power | 0x0003-0x0004 | ÷10 (W)
Energy | 0x0005-0x0006 | ÷1000 (kWh)
Frequency | 0x0007 | ÷10 (Hz)
Power Factor | 0x0008 | ÷100
2. PZEM-004T Communication (pzem_* functions)*_
Communicates via Modbus RTU over UART:
  Uses CRC-16 Modbus checksum for data integrity
  Reads every 5 seconds (pzem_read_interval = 5000)

## Slide 39
Route | Function
/ | PZEM dashboard with auto-refresh (AJAX every 5s)
/api | JSON data: {"voltage":220.1,"current":0.5,...}
/setup | WiFi configuration form
/save?ssid=X&pass=Y | Saves credentials and reboots
3. Web Server (start_web_server, handle_web_client)
Non-blocking socket server on port 80 with routes:
4. LCD 16x2 (I2C) (lcd_* functions)*_
  Line 1: IP address
  Line 2: Current (A) and Voltage (V)
  Auto-detects I2C address (0x27 or 0x3F)

## Slide 44: Workshop #4 : esp32-pzem-url.py
ESP32 PZEM Monitor with Remote Data Sending - Explanation
This is an enhanced MicroPython program for ESP32 that monitors AC power via PZEM-004T, displays on LCD, serves a web dashboard, and sends data to a remote server at configurable intervals.

## Slide 53
Use Case
This is an industrial IoT power monitoring system that:
  Measures AC voltage/current/power/energy from machinery
  Displays real-time values locally on LCD
  Provides web dashboard for remote viewing
  Logs data to cloud server for historical tracking/analytics
  Supports multi-device deployments via unique dev_id/mc_id

## Slide 55
Backend

## Slide 57
https://www.php.net/

## Slide 58: Backend Software
https://www.phpmyadmin.net/

## Slide 59
https://grafana.com/grafana/download

## Slide 61: การติดตั้ง Software บน Cloud Server
https://m.do.co/c/fbc7a836fe39

## Slide 74
Click

## Slide 79
List files
Change directory
Edit file
Select & Click Left
Copy
Exit use Ctrl+x
d1799b3c534f958ac1e9bf09f34b46ae78cc10a1156a9169
d1799b3c534f958ac1e9bf09f34b46ae78cc10a1156a9169

## Slide 83
http://137.184.86.182/iot2025/e089/insertE1.php?devid=e089&mcid=m-001&amp=0.000&volt=234.1&pf=0.00&energy=0.24

## Slide 87: Create php file
http://137.184.86.182/iot2025/e089/insertE1.php?devid=e089&mcid=m-001&amp=0.000&volt=234.1&pf=0.00&energy=0.24

## Slide 88
https://github.com/drpasidth/esp32_pzem/blob/main/insertE1.php

## Slide 89
Change to http://188.166.252.164/

## Slide 90
Stop and Upload

## Slide 94: Install Grafana
https://github.com/drpasidth/esp32_pzem/blob/main/grafana

## Slide 97: Set Server

## Slide 103
SELECT volt FROM iot_db.electric LIMIT 50

## Slide 111
SELECT volt FROM iot_db.electric LIMIT 50

## Slide 112
Q & A